SRResNet [1]

SRResNet is the generative network for the SRGAN.

- 16 residual blocks
- omits the Relu in the original resnet after addition [2]
- use Prelu instead of relu
- two trained sub-pixel convolution layers for increasing the resolution of the input image[3]
- trained using the cost function based on MSE and VGG22. SRResNet-MSE get good results on the PSNR test.

Result: removal of a 4-pixel wide strip from each border
4x	PSNR	SSIM
Set5	32.05	0.9019
Set14	28.49	0.8184
BSD100	27.58	0.7620

Training details:
-training set: random sample of 350 thousand images from ImageNet
- batch: 16 images, 96 x 96 HR sub images of distinct images.
-size: input 24x24 label 96x96
- feature scaling: LR [0,1], HR[-1, 1]
-learning rate: 10**-4, no decay mentioned
-iterations: 10**6
-optimizer: Adam beta1 = 0.9

VDSR [4]

ideas:
- Depth is helpful for increasing the receptive field for large image context
- residual learning allows high learning rate and faster convergence 0.1, also better performance can be used in SR case, input and output are similar
- gradient clipping: clip the gradients to [-theta/gamma, theta/gamma], makes the convergence much faster (4 hours) theta range, gamma learning rate

- In the experiment, 20 weighted layers (conv layers)
- batch norm not mentioned
- filter 3*3*64
- activation: relu
-cost func: MSE

Training details:
-training set: use 291 images as in [5] for benchmark with other
methods in this section
-optimizer: mini batch gradient descent with momentum 0.9
-regularization: L2 * 0.0001
- learning rate: was initially set to 0.1 and then decreased by a factor of 10 every 20 epochs, 3 times in total
- batch size: 64 sub-images, where sub-images from different scales can be in the same batch.
- Input size: equal to the size of the receptive field, related to length 41 * 41
- feature scaling: not mentioned
- iterations: 80 epochs (9960 iterations)
- data augmentation: rotation and flop

Results:

DRRN (Image Super-Resolution via Deep Recursive Residual Network) [6]

ideas:
- The deeper the better
- fewer parameters 2×, 6×, and 14× fewer parameters than VDSR, DRCN, and
RED30, respectively
- global residual learning + local residual learning
- recursive learning , proposed in DRCN [6]

Structure:

- residual block: green box
- recursive block: red box, concatenate connection, more recursions are performed in the recursive layer
- The red dashed box refers to a recursive block consisting of two residual units. In the
recursive block, the corresponding convolutional layers in the residual units (with light green or light red color) share the same weights
- activation: BN + Relu, pre-activation before weight layer, same as Resnet
- chain model(a) vs multi-path(d): multi-path is less prone to overfitting
- loss func: MSE
- global residual learning
- in experiment B = 1 (number of recursive block), U = 25 (number of residual blocks)

training details:
-gradient clipping [-0.01/gamma, 0.01/gamma] gamma is learning rate
- training set: 291 images, where 91 images are from Yang et al. [7] and other
200 images are from Berkeley Segmentation Dataset [8].
-data augmentation: flipped and rotated, 90 ◦ , 180 ◦ , 270 ◦ and flip
them horizontally
-scale augmentation included *2 *3 *4 in a single model
- patch size: 31 × 31 patches, with the stride of 21
- optimizer: mini-batch size of SGD to 128, momentum parameter to 0.9, and weight decay to 10 −4
- filter size: 3 *3 * 128
- learning rate: 0.1 and then decreased to half every 10 epochs
- initialization: same as [9]
- iterations: not mentioned
- feature scaling: not mentioned

Result:

another metric proposed: Information Fidelity Criterion [10]

claims to have the highest correlation with perceptual scores for SR evaluation

PS: also a study about the depth: number of B,U, same depth will lead to comparable results

SRDenseNet

EDSR/MDSR > SRResNet > SRDenseNet > DRRN > DRCN > VDSR > SRCNN

idea:
- the SR performance can be further improved
both in terms of accuracy and speed by learning the upscal-
ing filters
- skip connections
-fusion of features at different levels
SR

-DenseNet block: feature maps are concatenated

- the tmp new feature maps are computed from the old feature map and concatencated to the old feature maps to achieve the final new feature map. The further new feature map is computed from the new feature map with (channel increasing) and concatenated to them.
- activation: relu
- 8 convs in one dense block with growth rate k = 16
- 8 desnet blocks
- deconv layer: 2 successive layers with 3 * 3 kernels and 256 feature maps

training details:
- training set: 50000 images were randomly selected from ImageNet.
- SR performed in the luminance channel (Y channel of YcbCr)
- input size: 100 x 100
- optimizer: adam
-initialization: bias 0, weights according to [11]
- learning rate: 0.0001 decrease by factor of 10 after 30 epoches
- batch size: 32

*Deep image prior:
idea:
- the structure of a generator network is sufficient to capture a great deal of low-level image statistics prior to any learning.
- a great deal of image statistics are captured by the structure of a convolutional image generator rather than by any learned capability
- randomly-initialized generative network can be used to sample realistic images from a random distribution
- using am encoder-decorder “hourglass” architecture with as many as two mil-
lion parameters θ
- In terms of (1), the prior R(x) defined by (2) is an in-
dicator function R(x) = 0 for all images that can be pro-
duced from z by a deep ConvNet of a certain architecture,
and R(x) = +∞ for all other signals
- for most applications, restrict the number of iterations in the optimization process
(2) to a certain number of iterations.

Result:
While our method is still outper-
formed by learning-based approaches, it does considerably
better than bicubic upsampling. Visually, it seems to close
most of the gap between bicubic and state-of-the-art trained
ConvNets

mentioned: perceptual loss[12] and adversarial loss (in SRGAN)

[1] Photo-Realistic Single Image Super-Resolution Using a Generative Adversarial Network.
[2] S. Gross and M. Wilber. Training and investigating residual nets, on-
line at http://torch.ch/blog/2016/02/04/resnets.
Html.
[3] W. Shi, J. Caballero, F. Huszar, J. Totz, A. P. Aitken, R. Bishop,
D. Rueckert, and Z. Wang. Real-Time Single Image and Video
Super-Resolution Using an Efficient Sub-Pixel Convolutional Neural
Network. In IEEE Conference on Computer Vision and Pattern
Recognition (CVPR), pages 1874–1883, 2016. 3, 4, 5, 6, 7, 8

[4] Accurate Image Super-Resolution Using Very Deep Convolutional Networks
[5] Fast and accurate image upscaling with super-resolution forests.
[6] Deeply-Recursive Convolutional Network for Image Super-Resolution
[7] Image super-resolution via sparse representation.
[8] A database of human segmented natural images and its application to
evaluating segmentation algorithms and measuring ecologi-
cal statistics.
[9] Delving deep into rectifiers: Surpassing human-level performance on ImageNet
classification.
[10] Single image super-resolution from transformed self-exemplars
[11]Delving deep into
rectifiers: Surpassing human-level performance on imagenet
classification.
[12] Perceptual losses for
real-time style transfer and super-resolution.